## Slide 1: How to Deal with Geomagnetic Storms in Directional Drilling
Inge Edvardsen
PhD Candidate/Survey Management Engineer

## Slide 2: Directional Drilling
Directional drilling is the practice for drilling non-vertical wells.
MD [m] | INC° | AZI°
0 | 0 | 0
30 | 0 | 0
... |  | 
1000 | 90 | 180
... |  | 
5000 | 90 | 90
Wellpath

## Slide 3: Magnetic Directional Surveying
The accuracy of magnetic azimuth decreases with increasing latitude due to:
  Magnetic north is more difficult to resolve because of smaller signal strength.
  Increased time dependent fluctuations in the orientation of the magnetic field, magnetic storms (The disturbance field).

## Slide 4: Earth’s Magnetic Field - Main Characteristics

## Slide 5: Earth’s Magnetic Field - Components
Bm - Main field
Bd - Disturbance field
Bc - Crustal field

## Slide 6
The Disturbance Field –
The Auroral Electrojet
Bm - Main field
Bd - Disturbance Field
I - Auroral Electrojet

## Slide 7
Monitoring the Disturbance Field
Bm - Main field
Bd - Disturbance Field
I - Auroral Electrojet
- Variometer station
Jäckvik
Dønna
Rørvik

## Slide 8
Monitoring the Disturbance Field
Finnish geomagnetic observatories and stations
Norwegian geomagnetic observatories and stations

## Slide 9: The Disturbance Field – Magnetic Storm
Magnetic storm at Dønna
6th August 2011
The green area indicates the MWD error model disturbance limits.
F [nT] | D [deg] | I [deg]
+/- 147 | +/- 0.45 | +/- 0.18

## Slide 10
When any of the error model disturbance limits are exceeded:
  A sms and an e-mail is transmitted to service companies.
  The Survey Management engineer evaluates the situation og gives recommendations to the offshore rig sites.
UIT Warning System

## Slide 11: Why Deal with the Disturbance Field
It is neccessary to manage such disturbances to have directional control while drilling.
  Hit the geological target and maximize the recovery
  Avoid other wells
Survey QC tests may identify an out of spec condition, and monitoring of the field can differentiate between tool failure and field disturbance.
  Avoid unnecessary pull outs
Accurate monitoring may allow correction for disturbance effects.

## Slide 12: Hit the Geological Target

## Slide 13: Avoid Other Wells

## Slide 14: Monitoring in the Norwegian Sea
Norwegian Sea
Barents Sea
- Oil & Gas Fields
200 km
RØR
DØN
JAC
- Monitoring Station (Variometer)

## Slide 15: Conclusions
To have directional control while drilling is important for several reasons:
  Hit the geological target and maximize the recovery
  Avoid other wells
  Avoid unnecessary pull outs
Monitoring the external magnetic field is vital for achieving this.

## Slide 16: Thank You for Listening